## Slide 1
THERMOMETRY
B.Sc. II Physics • 08 Hours
Heat → Temperature → Measurement
Dr. Sandip S. Patil
Associate Professor of Physics

## Slide 2
Learning Outcomes
OVERVIEW
• Distinguish the physical concepts of heat and temperature.
• Explain the principle of thermometry and identify thermometric properties.
• Describe common types of thermometers and temperature scales.
• Convert temperatures among Celsius, Kelvin, Fahrenheit and Rankine scales.
• Explain the construction, working, errors and corrections of a mercury thermometer.
• Explain Seebeck effect and the working of a thermoelectric thermometer.
• Describe the principle and operation of a platinum resistance thermometer.
Thermometry • B.Sc. II Physics | 2

## Slide 3
Heat and Temperature
BASIC CONCEPTS
Heat
Energy transferred between bodies because of a temperature difference. SI unit: joule (J).
Temperature
A measure of the thermal state of a body; it determines the direction of spontaneous heat transfer.
Heat flows spontaneously: higher T → lower T
• Temperature is an intensive property; heat is an energy-transfer quantity.
• Thermal equilibrium occurs when two systems have the same temperature and there is no net heat flow.
• Thermometry provides a reproducible numerical measure of temperature.
Thermometry • B.Sc. II Physics | 3

## Slide 4
Principle of Thermometry
BASIC CONCEPTS
A thermometer uses a measurable physical property that varies predictably with temperature.
Volume
Liquid expansion
Pressure
Gas pressure
Resistance
Electrical resistance
Thermoelectric emf
Seebeck effect
Radiation
Thermal radiation
Calibration connects the thermometric property to a defined temperature scale.
Thermometry • B.Sc. II Physics | 4

## Slide 5
Types of Thermometers
THERMOMETERS
Liquid-in-glass
Mercury / alcohol Property: Volume expansion
Gas thermometer
Constant V or P Property: Pressure / volume
Resistance thermometer
Pt, Ni, etc. Property: Electrical resistance
Thermocouple
Two dissimilar metals Property: Thermoelectric emf
Radiation thermometer
Non-contact Property: Thermal radiation
Thermometry • B.Sc. II Physics | 5

## Slide 6
Temperature Scales
TEMPERATURE SCALES
°C
100
0
100 divisions
K
373.15
273.15
100 divisions
°F
212
32
100 divisions
°R
671.67
491.67
100 divisions
Reference points
Water's ice point and steam point were historically used for Celsius and Fahrenheit calibration; modern SI temperature is based on the kelvin.
Thermometry • B.Sc. II Physics | 6

## Slide 7
Relations Between Temperature Scales
TEMPERATURE SCALES
C/5 = (F − 32)/9 = (K − 273.15)/5 = (R − 491.67)/9
Celsius ↔ Kelvin
K = °C + 273.15 °C = K − 273.15
Celsius ↔ Fahrenheit
°F = (9/5)°C + 32 °C = (5/9)(°F − 32)
Celsius ↔ Rankine
°R = (9/5)K °R = (9/5)(°C + 273.15)
Important
Temperature intervals: 1 K = 1 °C in magnitude. Absolute zero = 0 K = −273.15 °C.
Thermometry • B.Sc. II Physics | 7

## Slide 8
Worked Temperature Conversion
TEMPERATURE SCALES
Example
Convert 25 °C into Kelvin, Fahrenheit and Rankine.
K = 25 + 273.15 = 298.15 K
°F = (9/5)(25) + 32 = 77 °F
°R = (9/5)(298.15) = 536.67 °R
Check
All four values describe the same thermal state; only the numerical scale and zero point differ.
Thermometry • B.Sc. II Physics | 8

## Slide 9
Mercury Thermometer — Principle
LIQUID-IN-GLASS THERMOMETER
Thermometric property: volume of mercury
• Mercury expands approximately uniformly over a useful temperature range.
• The expansion is communicated to a narrow capillary, producing a measurable change in column length.
• At a fixed reference point, the observed column length can be related to temperature after calibration.
• Mercury is suitable because it is visible, does not wet glass appreciably, and has a relatively high boiling point.
Thermometry • B.Sc. II Physics | 9

## Slide 10
Mercury Thermometer — Construction
LIQUID-IN-GLASS THERMOMETER
Capillary
Mercury column
Bulb / reservoir
Graduated stem
100
80
60
40
20
Glass envelope
Protects the mercury and provides a stable capillary path.
Bulb
Contains most of the thermometric liquid and is placed in thermal contact with the object.
Capillary
Small cross-sectional area magnifies the change in mercury volume into a visible length change.
Thermometry • B.Sc. II Physics | 10

## Slide 11
Mercury Thermometer — Working
LIQUID-IN-GLASS THERMOMETER
Cold
Hot
thermal contact
Working sequence
1. Bulb is placed in thermal contact with the body. 2. Mercury expands or contracts. 3. Column moves in the capillary. 4. Scale reading gives temperature after calibration.
Thermal equilibrium
Accurate measurement requires sufficient time for thermometer and object to approach the same temperature.
Thermometry • B.Sc. II Physics | 11

## Slide 12
Mercury Thermometer — Errors
LIQUID-IN-GLASS THERMOMETER
Calibration / scale error
Incorrect reference-point or graduation calibration.
Parallax error
Eye not at the level of the mercury meniscus.
Stem / emergent-column error
Part of the mercury column is outside the region whose temperature is being measured.
Thermal lag
Reading taken before the thermometer reaches thermal equilibrium.
Capillary irregularity
Non-uniform bore changes the relation between volume and length.
Zero-point shift
Glass and mercury may show changes after repeated heating or aging.
Thermometry • B.Sc. II Physics | 12

## Slide 13
Mercury Thermometer — Corrections
LIQUID-IN-GLASS THERMOMETER
Parallax correction
Place the eye perpendicular to the scale at the level of the mercury meniscus.
Stem correction
Determine the average temperature of the emergent mercury column and apply the appropriate correction when required.
Calibration correction
Compare readings against fixed points or a standard thermometer and prepare a correction curve/table.
Thermal correction
Allow adequate time for equilibrium; use good thermal contact and minimize heat exchange with surroundings.
Practical care
Keep the bulb fully immersed where appropriate, avoid contact with container walls, and read the meniscus consistently.
Safety
Mercury is toxic. Modern laboratories often prefer digital, alcohol, resistance or thermocouple thermometers.
Thermometry • B.Sc. II Physics | 13

## Slide 14
Seebeck Effect
THERMOELECTRIC THERMOMETRY
Cold junction
Hot junction
E = f(T_hot − T_cold)
• When two dissimilar conductors form a closed circuit and their junctions are at different temperatures, a thermoelectric emf is produced.
• This is the Seebeck effect.
• The emf depends on the temperature difference and the materials used.
• A calibrated thermocouple converts measured emf into temperature.
Thermometry • B.Sc. II Physics | 14

## Slide 15
Thermoelectric Thermometer — Principle and Construction
THERMOELECTRIC THERMOMETRY
Principle
Uses the Seebeck effect: temperature difference between two junctions produces a measurable emf.
Construction
Two dissimilar metal/alloy wires are joined at the measuring junction; the reference junction is maintained or compensated at a known temperature.
Measuring junction
Reference junction
Metal A
Metal B
Common thermocouples
K, J, T, E, N, R, S and B types are selected according to temperature range, sensitivity and environment.
Thermometry • B.Sc. II Physics | 15

## Slide 16
Thermoelectric Thermometer — Working
THERMOELECTRIC THERMOMETRY
1
Hot junction
Place measuring junction in contact with the object.
2
Temperature difference
A difference exists between measuring and reference junctions.
3
Seebeck emf
A thermoelectric emf develops in the circuit.
4
Measurement
A sensitive voltmeter / millivoltmeter measures emf.
5
Calibration
Convert emf to temperature using a standard calibration curve/table.
Temperature ↔ Thermoelectric emf
Advantages
Wide temperature range, rugged sensor, small size, fast response and useful for remote measurements.
Limitations
Needs calibration; reference-junction compensation is required for absolute temperature measurement.
Thermometry • B.Sc. II Physics | 16

## Slide 17
Platinum Resistance Thermometer (PRT) — Principle
RESISTANCE THERMOMETRY
R(T) changes predictably with temperature
• Platinum has a stable and reproducible electrical resistance–temperature relationship.
• An electrical current is passed through a platinum sensing element and its resistance is measured.
• Temperature is obtained from the calibrated R–T relation.
• PT100 is a common sensor: nominal resistance is 100 Ω at 0 °C.
Why platinum?
High chemical stability, reproducibility, nearly linear response over a useful range, and excellent long-term stability.
Measurement principle
A resistance bridge or precision electronic measurement circuit determines the sensor resistance with high accuracy.
Thermometry • B.Sc. II Physics | 17

## Slide 18
PRT — Construction and Working
RESISTANCE THERMOMETRY
Platinum wire / thin film
Protective support / sheath
Sense
Measure R
Convert
Use R–T relation
Display
Read T
R = R₀[1 + α(T − T₀) + …]
Linear approximation over a limited range
Working
Temperature changes the resistivity of platinum → resistance changes → electrical circuit measures R → calibration converts R to T.
Thermometry • B.Sc. II Physics | 18

## Slide 19
Comparison of Thermometers
SYNTHESIS
Thermometer | Property | Main advantage | Main limitation | Typical use
Mercury | Liquid volume | Simple, visible reading | Limited range; toxic mercury | Traditional laboratory use
Thermocouple | Thermoelectric emf | Wide range, fast, rugged | Needs calibration/reference compensation | Industrial & laboratory
PRT / Pt100 | Electrical resistance | High accuracy & stability | More expensive; wiring effects | Precision temperature measurement
Gas thermometer | Pressure / volume | Primary-standard concept | Bulky and slow | Metrology / calibration
Selection principle
Choose the thermometer according to range, accuracy, response time, environment, stability and required calibration.
Thermometry • B.Sc. II Physics | 19

## Slide 20
Concept Check
ASSESSMENT
• 1. Distinguish heat from temperature.
• 2. What is a thermometric property? Give four examples.
• 3. Derive or use the relation connecting Celsius, Fahrenheit, Kelvin and Rankine scales.
• 4. Why is a narrow capillary used in a mercury thermometer?
• 5. Explain parallax and emergent-stem errors.
• 6. State the Seebeck effect and explain its application in thermometry.
• 7. Why is platinum preferred in resistance thermometry?
Thermometry • B.Sc. II Physics | 20

## Slide 21
Summary
RECAP
Heat & temperature
Heat is energy transfer; temperature characterizes thermal state.
Thermometry
A measurable thermometric property is calibrated against temperature.
Scales
Celsius, Kelvin, Fahrenheit and Rankine use different zero points and intervals.
Mercury thermometer
Uses thermal expansion of mercury; errors include parallax, stem, calibration and thermal lag.
Thermocouple
Uses Seebeck emf produced by a temperature difference between two junctions.
PRT
Uses predictable temperature dependence of platinum electrical resistance.
Measure a property → Calibrate → Determine temperature
Thermometry • B.Sc. II Physics | 21

## Slide 22
THERMOMETRY
From thermal state to quantitative measurement
Dr. Sandip S. Patil
B.Sc. II Physics